## Slide 1: Project ATLAS A thermomechanical analysis
Leonardo Ribeiro

## Slide 2: Introduction
Modules operate between -60 C and RT
Induced thermal stresses (thermal expansion, coupled components)
Module’s resistance to the thermal cycle

## Slide 3: Methodology
Finite Element Analysis (FreeCAD)
Results can be compared to UTS of materials
Checking references (University of Glasgow’s simulation)

## Slide 4: The Model
#1:The Box Model
  5 boxes
  Top to bottom: PCB flex (Copper and Kapton), glue (Araldite),sensor (Silicon), bump bonds (Aluminum) and RD53 chip (Silicon)

## Slide 5: The Model
Homogeneous materials
Ambient temperature going from 20 C to -60 C
Mechanical constraint at RD53’s bottom
All relevant dimensions taken from mechanical design sketches
Heat flow allowed and taken into account

## Slide 6: General results
Strain on the left, maximum stress on the right
Magnitudes – see next slides

## Slide 7: Qualitative
Soft glue expands the most, absorbing the forces between sensor and PCB
Stress concentrated at bump bonds (low UTS)

## Slide 8: Quantitative challenges
Limited post-processing options
Huge variation within each layer, even for high element density
0.5 mm on the left, 0.3 mm on the right

## Slide 9: Quantitative challenges
Maximum stresses were too high due to deviations
Results not symmetric about origin as expected
Better post-processing needed

## Slide 10: Stress profile
Estimate based on cuts
Software constraint on step size (100 microns)

## Slide 11: Comparative analysis
LBNL
Stress concentrated at bump bonds
Magnitude of stresses still unclear
Semi-continuous stress profile
Model – glue as a box
Glasgow (Cunningham)
Maximum stress at Silicon sensor
Magnitudes calculated or estimated
One data point per layer
Model – glue pattern

## Slide 12: Conclusion
Despite uncertainties, major disagreement at location of concentrated stress
Allowing room for all cited errors, results still diverge significantly only at bump bonds

## Slide 13: Next steps
Finish data post-processing
Contact Glasgow team and look for source of disagreement
Refine model and move to single module
  Shape of bonds
  PCB details
  Heat source at RD53
  Wire bonds